## Slide 1
Bacterial contamination and greenhouse gas emissions – a randomized study of reuse versus single-use of infusion-set components for intravenous anaesthesia
Snorri Laxdal Karlsson, Jon Edman Wallér, Magni Vidar Gudmundsson, Peter Bentzer, Per Werner Moller

## Slide 2: Bacterial contamination and greenhouse gas emissions - a randomised study of reuse versus single-use of infusion-set components for intravenous anaesthesia
348 procedures included after randomisation: reusing infusion-set components marked in green vs. single-use of all components
Karlsson et al. Eur J Anaesthesiol. September 2024
@EJA_Journal
Reusing infusion-set components
Allowed three procedures per infusion set
Did not increase bacterial contamination
Reduced climate emissions by 69%
Single-use
Reuse

## Slide 4
Anti-reflux valves
10 cm infusion line with
three-way stopcock
Reused for several procedures
Sampling site
Built-in anti-reflux valve
Replaced between patients
Replaced when empty

## Slide 7
HSLF-FS 2021:32
EU 2017/745 (MDR)

## Slide 8
HSLF-FS 2021:32

## Slide 9
Prevalens av bakteriell kontaminering för varje metod
Jämföra klimatpåverkan mellan metoderna

## Slide 10
Prevalens av bakteriell kontamination okänd på avdelningen?
  Tidigare studier: 6-33%
Acceptabel prevalens? Klinisk signifikans?
150 procedurer per metod
  >10%
  <10%

## Slide 11
Inklusion och randomisering:
  operationssalar där >1 operation planerades
Registrerade:
  metod
  duration
  antal interaktioner med infusionssetet
  tillförd mängd läkemedel
  kvarvarande mängd läkemedel
  turordning

## Slide 12
Injektioner i trevägskranen
Opslut:
  Infusionsslangen kopplas från pvk
  Infusionsvätskan flyttas till aerob odlingsflaska.

## Slide 13
Operating rooms eligible for inclusion*
(n=108)
Procedures allocated to reuse (n=194)
Did not receive allocated intervention (n=1):
Blood pressure measured in TIVA infusion arm
Received allocated intervention (n=193)
Procedures allocated to single use (n=165)
Did not receive allocated intervention (n=2):
Incorrect assembling of infusion set
Received allocated intervention (n=163)
Allocation
Follow up
Analysis
Lost to follow up (n=2):
Two samples injected into the same culture bottle
Lost to follow up (n=2):
Forgot to take sample
No time to secure sample due to clinically challenging emergence from anaesthesia
Excluded from analysis (n=2):
Protocol violated by administering antibiotics via TIVA infusion set
Analysed (n=159)
Excluded from analysis (n=2):
Protocol violated by administering antibiotics via TIVA infusion set
Analysed (n=189)
Operating rooms randomised to manage procedures by reuse
(n=54)
Operating rooms randomised to manage procedures by single use
(n=54)
Randomisation

## Slide 14
4/348 - 1,15% kontaminering
Micrococcus – metod A, 3/3
Staph epidermidis – metod A 3/5
Staphylococcus – metod B
Staph epidermidis – metod B
vid flergångsanvändning kasserades mindre läkemedel
Propofol - minskning med 63%
Noradrenalin – minskning med 56%
Ingen skillnad mellan metoderna
3 procedurer per infusions-set
Studien hade styrka (power) att upptäcka absolut risk-skillnad på 6,4%
13 interventioner per infusions-set
Remifentanil – minskning med 67%

## Slide 15
6 min 49 sek
44 sek

## Slide 16
Prevalens av bakteriell kontaminering för varje metod
Jämföra klimatpåverkan mellan metoderna

## Slide 18
Chart: kg CO2-eq per median procedure
| Partial reuse (n = 189) | Single use (n = 159)
Component production | 0.18475 | 0.634
Medication production | 0.013017 | 0.012742
Packaging material | 0.023037 | 0.070424
Transport of medications and components | 0.060733 | 0.12978
Component waste handling | 0.129 | 0.447
Medication waste handling | 0.029187 | 0.076677
0.013
0.061
0.029
0.129
0.023
0.185
0.013
0.130
0.077
0.447
0.070
0.634
 0.43 (0.41-0.47)
 1.39 (1.37-1.40)
Greenhouse gas emissions
∆ -0.96 (-0.99 to -0.93)
P<0.0005
Reuse (n = 189)
Single use (n = 159)

## Slide 19
1,16 kg CO2-eq
0,07 kg CO2-eq

## Slide 20
Chart: kg CO2-eq per median procedure
| Partial reuse (n = 189) | Single use (n = 159)
Component production | 0.18475 | 0.634
Medication production | 0.013017 | 0.012742
Packaging material | 0.023037 | 0.070424
Transport of medications and components | 0.060733 | 0.12978
Component waste handling | 0.129 | 0.447
Medication waste handling | 0.029187 | 0.076677
0.013
0.061
0.029
0.129
0.023
0.185
0.013
0.130
0.077
0.447
0.070
0.634
 0.43 (0.41-0.47)
 1.39 (1.37-1.40)
Greenhouse gas emissions
∆ -0.96 (-0.99 to -0.93)
P<0.0005
Reuse (n = 189)
Single use (n = 159)

## Slide 21
Låg prevalens av bakteriell kontamination i båda metoder
  mkt större studie behövs för att hitta skillnad mellan metoderna
Återanvändning av infusions-set minskar klimatavtrycket

## Slide 22
per.moller@vgregion.se
snorri.laxdal.karlsson@vgregion.se